## Slide 1: LACCF Worship Team
Public Address System Installation and Training
10/30/2022
Updated on 08/25/2023
Updated on 04/03/2024

## Slide 2: Outline
Some basics of Public Address (PA) system
Our PA system
  Hardware and software
  User’s manual

## Slide 3: Public Address (PA) System
Outputs
Inputs
Mixer

## Slide 4: A Glimpse of Our PA System
Mixer
  Behringer X32 rack (22 IN, 14 OUT)
  DELL PC for control and audio interfaces
Inputs:
  2 wired microphones (SM58)
  GTD G-787 wireless microphone receiver
    wireless bodypack x2
    wireless handhold x2
  2 keyboards
  HDMI audio input through AUX ports
  PC audio through X32 audio interface (X-USB)
  1 guitar (with built-in pickup)
  1 violin (needs pickup)
Auxiliaries
  Power conditioner
  Power extension cord and outlets
  Digital Stage box Behringer SD16, 16 Input, 8 Output
  Snake cable, 8 sends, 4 returns
  DI boxes (for active/powered inputs)
Outputs
  Main output
    Speaker power amplifier (Behringer NX3000)
    Two wall-mounted speakers (Left & Right)
  Monitors
    Headamp-powered in-ear monitors for singers 1
    Battery-powered in-ear monitors for singers 2
    Headamp-powered in-ear monitors for pianists 1
    Battery-powered in-ear monitors for pianists 2
  Other outputs
    Digital audio for live streaming
    FM radio for the next-door
    Headphone at the console (for monitoring)

## Slide 5: PA System – Signal Flow
Dell desktop PC
Behringer X32 rack – digital mixer
(with built-in audio interface)
Ethernet cable for control console
Loudspeakers
Behringer SD16
16 in x 8 out
GTD Audio G-787 wireless mic
(bodypacks and handhelds)
HDMI Switch/Splitter
HDMI cable
Audio extracted
3.5 mm to RCA
USB cable for audio interface
Sound Blaster K3+
Audio interface
USB cable
Aux Out
NX3000 Amplifier
Main LR
FM transmitter
Aux Out
Aux In
Headamp >> In-ear monitors
Microphones (SM58), Keyboards, Guitar
Stage snake
Active in-ear monitor
Other instruments
Front stage – left side
Front stage – right side
Wall-mount
Headamp >> In-ear monitors
Active in-ear monitor

## Slide 6: Signal Flow inside a mixer

## Slide 7: Signal Levels: mic/line/speaker
Typical voltage
Mic: 0.001 – 0.1
Line: 0.1 – 10.0
Speaker: 10 - 100

## Slide 8: Decibel

## Slide 9: Gain: the most important parameter
Avoid too small, for the sake of good signal/noise ratio and good dynamical range
Avoid too large, otherwise feedback, or even sound will be clipped and/or distorted

## Slide 10: Impedance
SM58 microphone: 150 Ohm
Guitar pickup: easily beyond 10000 Ohm

## Slide 11: Feedback Loop

## Slide 12: Microphone Pattern

## Slide 13: Ground Loop

## Slide 14: DI Box: a solution of impedance matching and ground loop

## Slide 15: Cables: XLR/TRS/TS
Balanced
Balanced
unbalanced

## Slide 16: Balanced Noise Cancellation

## Slide 17: MixBus

## Slide 18: Reverb

## Slide 19: Fx (effect, e.g., reverb) Send/Return

## Slide 20: EQ/Comp/Gate ….

## Slide 21: Our PA System: Hardware and Software
Mixer
  Behringer X32 rack (22 IN, 14 OUT)
  Laptops for control and audio interfaces
Inputs:
  4 wired microphones
  4 wireless microphones
  2 keyboards
  Line-in from the Preach computer
  USB input from the console
  1 guitar (with built-in pickup)
  1 violin (needs pickup)
Auxiliaries
  Power conditioner, Furman M-8x2 8 outlets
  Power extension cord and outlets
  Digital Stage box Behringer SD16, 16 Input, 8 Output
  Snake cable, 8 sends, 4 returns
  DI boxes (for active/powered inputs)
Outputs
  Main output
    Speaker power amplifier (Behringer NX3000)
    Two wall-mounted speakers (Left & Right)
  Monitors
    Headamp x 2 (1 in 4 out)
    Battery-powered in-ear monitors x2
  Other outputs
    Digital audio for live streaming
    FM radiofor the next-door
    Headphone at the console (for monitoring)

## Slide 22: Digital Mixer: Behringer X32 Rack The heart of our PA system

## Slide 23: X32 Rack Built-in Audio Interface (i.e., the “card”) we use it for streaming and multimedia playback

## Slide 24: Digital Stage Boxes
Behringer SD16
pro snake CAT6E Cable

## Slide 25: Power Amplifier: Behringer NX3000 Please keep the settings unchanged (tuned once, and for all)

## Slide 26: Power Conditioner: Furman M-8x2 For cleaner power supply

## Slide 27: DI Box: EWI FDB-101 Passive DirectBox for active/powered inputs (ex: pre-Amp guitar)

## Slide 28: FM Transmitter Sending audio to the next door (Frequency 87.5)

## Slide 29: Headphone Amplifier Our wired in-ear monitors (1 input, 4 outputs, Piano side)
Can work with the passive in-ear monitor below so that to allow musicians to adjust volume by themselves

## Slide 30: Behringer HA-400 Ultra Compact 4-Channel Stereo Headphone Amplifier
Can work with the passive in-ear monitor below so that to allow musicians to adjust volume by themselves
For wired in-ear monitors (Singer side)

## Slide 31: Active In-ear Monitors Possible to customize a mix out for each channel
Behringer P2 Ultra-Compact Personal In-Ear Monitor Amplifier (Battery-powered)
YINYOO KZ ZSN PRO in-Ear Headphones HiFi Noise-isolating in Ear Monitor

## Slide 32: Our Microphones
Shure SM58
GTD Audio G-787

## Slide 33: X32 Rack Hook-up
IN 1-2 Computer audio in
IN 3-4 HDMI audio in
IN 5-8 not in use
IN 9–12 << wireless microphone receiver
IN 13-16 not in use
Aux IN 1-6 not in use
OUT 1-2 not in use
OUT 3-4 >> FM transmitter >> the next-door FM receiver and speakers
OUT 5-6 >> Sound Blaster K3+ audio interface >> computer for OBS streaming
OUT 7-8 >> power amp (NX300) Channel A-B >> two wall-mounted speakers
Aux OUT 1-6 not in use
Aux OUT 5-6
USB 2.0 port <> the computer for live streaming and playback but we don’t use it (see slide 50)
Ethernet port <> (can add Router here) <> the computer for mixer control console
“FW 400” port – not in use
MIDI in/out– not in use
UltraNet– not in use
AES50 A – use CAT6E Cable connect to Behringer SD16 (next page)
AES50 B– not in use
Talkback/monitor - not in use
AC input << power conditioner

## Slide 34: Behringer SD16 Hook-up
INPUT
  A 01-02 not in use
  A 03-04 << wired microphone (Vocal Mic k1 k2)
  A 05-06 << Keyboard (Keybd k1 k2)
  A 07-08 not in use
  A 09 << snake A << Guitar on the Right of the stage
  A 10-16 << snake B-J not in use
OUTPUT
  OUT 1 << X32 output 9 (Bus 3) >> Pianist 1 Monitor
  OUT 2 << X32 output 10 (Bus 4) >> Pianist 2 Monitor (battery powered Active In-ear Monitor)
  OUT 3-4 not in use
  OUT 5 << X32 output 13 (Bus 1) >> snake 1 >> Singer 1 monitor
  OUT 6 << X32 output 14 (Bus 2) >> snake 2 >> Singer 2 monitor (battery powered Active In-ear Monitor)
  OUT 7-8 >> snake 3-4 not in use
AC input << power extension cord on stage
USB not in use
AES50 A - use CAT6E Cable connect to X32
AES50 B not in use
OUT – switch set to 9-16

## Slide 35: X32 Rack Signal Routing mapping/customizing the physical sockets with internal signals

## Slide 36: Routing Inputs mapping the physical(socket)/USB inputs to the channels on the control panel
Channels 1-8 <- AES50 1-8
  wired microphones and instruments on stage
Channels 9-16 <- AES50 9-16
  Right of the stage through snake. Channel 9 used for Guitar
Channels 17-24
  Channels 17-18 <- Computer Audio in L and R
    the computer stereo will be fed to channels 17/18 (which should be linked)
  Channels 19-20 <- HDMI audio in
  Channels 21-24 <- Local IN 5-8 (Not in use)
Channels 25-32
  Channels 25-28 <- Local IN 9–12 (wireless microphones on the top of the audio rack)
  Channel 29-32 <- Local IN 13-16 (Not in use)
Here are the ”AES50”
This is the ”card, not used”
PC L and PC R in 01 02
HDMI In 03 04
Local In 5-8, 9-16

## Slide 37: Routing Outputs mapping the signals inside the mixer to the physical output sockets/USB outputs
OUT 1-2 <- MixBus 1
  We reserve MixBus 1 for monitors
OUT 3-4 <- Main L&R to FM transmitter >> the next-door FM receiver and speakers
OUT 5-6 <- MAIN L&R to Sound Blaster K3+ audio interface >> computer for OBS streaming
OUT 7-8 <- MAIN L&R
  The factory default reserves OUT 7-8 for the stereo MAIN LR
OUT 9-10 (AES50 OUT 1-2) <- MixBus 3-4
  Pianist 1 -2 Monitor
OUT 11-12 (AES50 OUT 3-4) <- MixBus 3
  Not in use
OUT 13-14 (AES50 OUT 5-6) <- Snake 1 -2 <- MixBus 1-2
  Singer 1 -2 Monitor
OUT 15-16 (AES50 OUT 7-8) <- Snake 3 -4 <- MixBus 1
  Not in use

## Slide 38: Routing Main LR (Pre-Fader+Mute)for Live Streaming
(Not In Use. Not updated)
We made a copy of MAIN LR (Pre-Fader + Mute) to OUT 9-10
Then we send/map OUT 9-10 to Card Outputs 1-8
On the computer, the copy of MAIN LR (Pre-Fader + Mute) will appear as “X-USB 1-2”
Therefore, we should feed “X-USB 1-2” to the streaming app ”OBS” as the “mic/aux in” (adjust the gain if necessary)

## Slide 39: Routing Main LR (Pre-Fader) Of Aux Out
(Not In Use. Not updated)
Send Main L to Aux 1 to FM transmitter >> the next-door FM receiver and speakers
Send Main LR to Aux Out 5-6 to utilize the TRS/RCA sockets to Sound Blaster K3+ audio interface >> computer for OBS streaming
Aux Out 2-4 not in use

## Slide 40: Power ON/OFF
Please follow the order below to turn ON the system:
  Power conditioner >> X32 rack >> power amplifier
Please follow the order below to turn OFF the system:
  Power amplifier >> X32 rack >> power conditioner

## Slide 41: Our PA System: user’s manual
How to connect X32 rack to computers and/or iPad
How to use the on-board control panel on X32 rack
How to set gain for microphones and other instruments
How to send signals to a MixBus, e.g., Main LR, monitors
How to use Fx (effects), e.g., reverb
How to use the mute groups
How to set Low Cut/Gate/Dyn/EQ
How to link channels (for stereo inputs)
How to save/load settings
How to set the limiters on the power amplifier
How to set up and use the monitors
How to set up audio for live streaming on computer
How to playback audio through the built-in sound card
How to do multitrack recording
Service routine check list
Trouble shooting

## Slide 42: How to tune the power amplifier Behringer NX3000 (once and for all)
The speakers and power amplifier much way more powerful than we may need (for some historical reason, we re-used the speakers). Therefore, we need to limit the output of the power amplifier.
The power amplifier just needs to be tuned once, and we should keep the settings unchanged, and fine the volume on the mixer. Below are how to initialize the settings:
  Before the procedure, make sure that the power amp is off and tune the level knobs to minimum;
  have a reference sound output from the mixer, make sure the averaged the output level around -18 dB. When observing the main out meter on the mixer panel, it should turn yellow from green frequently;
  Inject the output above to the power amp through Channel A and B;
  turn on the power amp, tune the level knobs up slowly, one click at a time. Listen to the main (loud) speakers, stop tuning up when it is loud enough.
  Keep the settings unchanged, fine tune the volume on mixer when needs.

## Slide 43: Video System – Hardware
Dell desktop PC
Epson ceiling-mount projector
Sony camera
HDMI switch and splitter (2 in 4 out)
HDMI extension
HDMI capture cards x2

## Slide 44: Video System – Signal Flow
Laptop for sermon
(the front computer)
Dell desktop PC
(the console)
HDMI switch/splitter
HDMI extension box
HDMI extension box
HDMI cable
HDMI cable
HDMI cable
ethernet cable
Epson projector
Duplicated signals thru HDMI cables
Wall-mount 55-inch TV
HDMI capture card
Sony camera
HDMI capture card
HDMI cable
USB cable
USB cable
Switch between the two inputs
Over ceiling

## Slide 45: HDMI Extension Deliver video/audio from front to console
Note: the limit length of HDMI cables ~ 50 ft

## Slide 46: HDMI Capture Card
For capturing the projector screen
For the live-streaming camera

## Slide 47: OBS as HDMI Switch? It would work, but put too much stress on the console computer! That is why we need a hardware solution for HDMI switching.

## Slide 48: HDMI Switch and Splitter The Heart of our video distribution system
Note that a single HDMI output could draw up to 300 mA at 5 V. We have 3 outputs from the box, so I recommend that the capacity of the power adopter should be > 2000 mA at 5 V.
We also extract audio from HDMI using this device and feed it to the mixer through the RCA aux input ports.

## Slide 49: Sending computer audio to PA system?
There are two options
  Through the HDMI switch/splitter, the audio can be extracted from HDMI and fed to the mixer via the RCA aux input ports. This method applies to both the console computer and the front laptop for sermon;
  Through the built-in audio interface onboard the X32 mixer. By default, the stereo audio should be sent through the “X-USB out-1/2” channels. This method applies only to the console computer.

## Slide 50: Audio Interface Mixer output for live streaming
Sound Blaster K3+
Why not using the built-in audio interface onboard the X32 mixer?
Theoretically, the X32 build-in audio interface is bi-directional, which means it should work for transferring the audio from the mixer to the PC (for live streaming).
But …
Practically, the audio interface is not stable, there are intermittent dropouts, which makes it unusable.

## Slide 51: Questions? Comments? Suggestions?

## Slide 52: Thank you for your contribution! Please email me if you have any questions ganzhaoming@gmail.com